!===============================================================================

!

! README for OMCLDRRG (OMI Daily L2G for OMCLDRR)

!

! Peter J.T. Leonard (ADNET) - 07/09/11

!

! OML2G High Level Overview:

!   This is the main program for the OML2G Product Generation Executive (PGE).

!

!   The OML2G PGE creates an Ozone Monitoring Instrument (OMI) daily Level 2G

!   (L2G) gridded data product file from (as many as) 16 OMI orbital Level 2

!   (L2) swath data product files.

!

!   Each OMI L2G product file contains 24 UTC hours of OMI L2 data from a single

!   OMI L2 product subsetted onto a longitude-latitude grid.

!

!   An OMI L2G day is defined to be the 24 hours that lie between UTC times of

!   0 hours, 0 minutes, 0 seconds and 23 hours, 59 minutes, 59.999999 seconds.

!

!   The OMI L2G product currently excludes L2 data collected in spatial and

!   spectral zoom modes.

!

!   The format of the OMI L2G product files is consistent with the document

!   entitled "HDF-EOS Aura File Format Guidelines" by C. Craig et al.

!

! OML2G Algorithm:

!   The OML2G PGE populates each cell in the L2G grid with data for all L2

!   "scenes" that

!   1) have observation times that lie within the L2G day in question,

!   2) have centers that lie within the L2G grid cell in question, and

!   3) are "good".

!

!   The OML2G PGE makes use of different definitions of "good" to populate

!   the L2G grids that correspond to different L2 products.

!

!   In the case of the OMI L2G product named OMCLDRRG, which is L2G for the L2

!   product named OMCLDRR, the definition of a "good" scene is one that has

!   i)  a solar zenith angle that is less than or equal to 88.0 degrees, and

!   ii) a cloud pressure that is not equal to the missing value.

!

!   The OMI L2 data that are reproduced in the OMI L2G product are not averaged

!   or weighted in any way by the OML2G PGE.

!

! Adopted L2G Grid:

!   The adopted L2G grid is a 0.25-degree by 0.25-degree grid in longitude and

!   latitude.  The dimensions of this grid are 1440 by 720.  The origin of the

!   grid is at lower left.  That is, the grid cell at coordinates (1, 1)

!   is centered at (longitude = -179.875 , latitude = -89.875),

!   and the grid cell at coordinates (1440, 720)

!   is centered at (longitude =  179.875 , latitude =  89.875).

!

!   Each "good" L2 scene is mapped onto only one L2G grid cell.

!

!   The number of L2 scenes that are mapped onto a given L2G grid cell can range

!   from 0 to 12.  These data are stored in an additional dimension of the grid.

!

!   The adopted L2G grid is consistent with the document entitled "Definition

!   of OMI Grids for Level 3 and Level 4 Data Products" by J.P. Veefkind et al.

!

!===============================================================================